USRP Receiver Front End
Design Document
SuperDARN
Revision 2
## Revision History
Description	Revision	Date	Author
Initial Document – John Klein’s Board	2	6/25/2018	Bryant Klug

# Introduction
## Purpose
The receiver front end board sits between the USRP and the power divider and is used to amplify the signal for the USRPs.
## Scope
# Reference Documents
Datasheets
https://www.idt.com/document/dst/f1912-datasheet – Attenuator
http://cdn.macom.com/datasheets/masw-007935.pdf – RF Switch
http://www.ti.com/lit/ds/symlink/trf37b73.pdf – RF Gain Block (amplifier)
http://www.skyworksinc.com/uploads/documents/SMP1330_Series_200050N.pdf – Limiter Diodes
https://www.minicircuits.com/pdfs/SCLF-25+.pdf – Low Pass Filter
https://www.lairdtech.com/products/bmi-s-207 – EMI Sheild
http://www.analog.com/media/en/technical-documentation/data-sheets/ADP7158.pdf – Voltage Reg.
# Overview
## Requirements
The SuperDARN operates in the HF band, between 8-20 MHz. Therefore all components need to operate in this range.
## Constraints
## Concept of Operation
There are three amplifiers and one attenuator in the RF path. Each amplifier provides about 15.5 dB of gain. Two of the amplifiers can be removed from the RF path through the AMPxn_CTRL lines. The attenuator is variable and can provide 0-31.2 dB of attenuation in 0.5 dB steps. The attenuator is controlled by a serial interface through the USRP.
There are three PIN limiters, one at the beginning, middle, and end of the receive line. (However it is not clear if these are necessary or even work at this low of frequency.)
There is an off the shelf low pass filter and a custom high pass filter after the first amplifier. There is an optional Pi filter in front of the USRP receiver connector for extra filtering.
The transmit line is routed directly to the phasing matrix. The receiver can be routed through the receiver path or it can be routed through the transmit path (for McMurdo).
The EMI shield was chosen so that it would fit over the low pass filter from Minicircuits, which is 7.1 mm tall. This was the only option on Digikey and Mouser at the time and it is 1.747” square (or 44.37 mm square).
## System Components
## Items of Concern
Signal path is not shielded. To reduce noise, the path should have ground vias on both sides, maybe have the trace down one layer and have a ground pour on top of the path.
Traces have 90 degree turns. These need to be removed.
Isolation happens at multiple places. There should be only one line that signifies the isolation between the phasing matrix and the USRP sides of the board.
Parts could be alligned to provide straight paths between parts.
Better silk screen. There are mistakes (Amp selection LED silk is wrong) and in some places the parts cover the RefDes.
Verify TR gate signal polarity throughout transmitter. Note from John on GitHub.
Jumpers in the signal path. These are bad for EMI, should be removed and replaced with 0 ohm resistors.
Signal is present on board with AMP1 turned on. Possibly from passives making a resonator.