USRP Receiver Front End
SuperDARN
Revision 2.1
## Revision History
Description	Revision	Date	Author
Initial Document	2.1	6/25/2018	Bryant Klug

# Introduction
## Purpose
The receiver front end board sits between the USRP and the power divider and is used to amplify the signal for the USRPs.
## Scope
# Reference Documents
# Overview
## Requirements
The SuperDARN operates in the HF band, between 8-20 MHz. Therefore all components need to operate in this range.
## Constraints
## Concept of Operation
There are three amplifiers and one attenuator in the RF path. Each amplifier provides about 15.5 dB of gain. Two of the amplifiers can be removed from the RF path through the AMPxn_CTRL lines. The attenuator is variable and can provide 0-31.2 dB of attenuation in 0.5 dB steps. The attenuator is controlled by SPI (Serial) through the USRP.
There are three PIN limiters, one at the beginning, middle, and end of the receive line. (However it is not clear if these are necessary or even work at this low of frequency.)
The transmit line is routed directly to the phasing matrix. The receiver can be routed through the receiver path or it can be routed through the transmit path (for McMurdo).
## System Components
## Items of Concern